## Slide 1: Introduction to water and water supply
Laban Sabiti

## Slide 2: Introduction
Water is a basic necessity for life.
Unfortunately, not all water helps human to survive.
Water from contaminated sources causes numerous diseases and untimely deaths.
The fact that a human needs water and cannot live without it forces him to use it even for drinking purposes, from any source, whether pure or contaminated, As a result, many people suffer or die from waterborne diseases.
Hence, every country has to take preventive measures to avoid pollution and contamination of the available water resources.
Therefore, public water supply must be potable, palatable and wholesome. Water must not have disagreeable physical change and must be hygienically safe.

## Slide 3: Importance of Water
Water is necessary in promoting personal hygiene and in cleaning the environment
Water is essential for life. Man can live nearly two months without food, but can live only three or four days without water.
In general 70% of human body weight is water and a human being needs two liters of water per day as minimum.
Most of the foods that man eats contain water. For example:
  Milk contains about 88% water.
  Egg contains about 66% water.
  Fish are 80% water.
  Potatoes are 75% water.
  Beef is 77% water
It is essential to run industries. Nearly all modern industries are thirsty; they need water.

## Slide 4: Importance of Water
It’s important for the balance in ecology (i.e. the balance in relationship between living things and the environment in which they live). All animal life depends directly or indirectly upon vegetation for food, and vegetation will not grow without water.
Water is important for agriculture, animal breeding and fishing
Water is a valuable source of energy. It is capable of generating hydroelectric power.
Water facilitates transportation and navigation.
Water plays an important role in recreation activities.

## Slide 5: Global Occurrence of Water
Water is located in all regions of the earth. The problem is that the distribution, quality, quantity and mode of occurrence are highly variable from one locality to another.
Water is the most widely occurring substance in the world.
Over 72% of the earth's surface is covered by water.
This means that if the body of water were evenly distributed, it would cover the globe to an average depth of over 4 kilometers.
Out of the 72% of the earth’s surface water, 97.2% is in the ocean, which is unfit for human consumption

## Slide 6: Properties of Water
Pure water consists of two atoms of hydrogen and one atom of oxygen chemically combined.
The chemical symbol is H2O and the chemical name is hydrogen monoxide
Water exists in three states: as a liquid, as a solid (ice and snow), and as a gas (water vapor).
It is a very stable chemical substance.
It boils at 100 degrees Celcius and freezes at 0 degrees Celcius at a barometric pressure of 760 millimeters of mercury

## Slide 7: Properties of Water
Pure water is practically colorless, odorless and tasteless. Any deviation from these physical characteristics should be considered as an indication of impurity.
Water has the ability to dissolve solids and to absorb gases and other liquids. Hence, it is often referred to as the “universal solvent”
Water has very high molecular attraction both for its own molecules (cohesion) and for molecules of other substance (adhesion)

## Slide 8: Sources of Water supply
Ground water sources
These include
  Open wells
  Deep wells
  Springs
  Infiltration
Surface water sources
These include;
  Lakes
  Rivers
  Ponds
  Streams
  Storage facilities from the rain harvest

## Slide 9: Groundwater
Groundwater may be defined as that portion of the total precipitation which has percolated downward into the porous space in the soil and rock where it remains, or from which it finds its way out to the surface.
Groundwater is by far the most practical and safe in nature.
It is the most important source of supply for most rural communities of the world. Examples of groundwater are wells and springs.

## Slide 10: Advantages
It is comparatively likely to be free from disease causing micro-organism
it can be used without further treatment if properly protected and treated immediately after the completion of construction work on the well or other source where groundwater is available.
It is not exposed for evaporation and is used as natural storage in underground.
It is most practical and economical to obtain and distribute.
Groundwater can be found near a family or a community

## Slide 11: Disadvantages
It needs pumping unless it comes from a spring
It may contain excess amounts of dissolved minerals.
It is poor in oxygen content.

## Slide 12: Springs
Are occurrences of groundwater naturally issuing at points where the water table reaches the surface, or where the top confining layer over the water – bearing strata is broken.
Springs are normally found at the foot of mountains and hills, in lower slopes of valleys, and near the banks of major rivers.
The yield (flow rate) of a spring varies with the position of the water table, which in turn varies with the rainfall amount at that locality and season.

## Slide 13: Classification of springs
Surface, intermittent or seasonal spring: These are springs which outcrop at a point higher in the groundwater body than the impermeable stratum in the ground formation.
These are in fact seepages from the subsoil or through cracks or faults in the rock formation.
These springs are usually not reliable, drying up during drier seasons and appearing again during or after the rainy seasons. They should not be developed as water supply sources unless observed throughout the year for their reliability.

## Slide 14
Mainsprings: These flow out of the ground after the infiltration water has reached an impermeable stratum in the rock layers. Such springs are sometimes known as gravity springs because the force of gravity makes them flows in the direction of the hydraulic gradient.
Thermal or hot springs: Are springs of water which haven been heated before they reach the surface of the ground.

## Slide 15
There are at least two explanations for the occurrence of thermal springs:
  Heat escaping from hot lower levels of the earth’s crust towards ground level may heat groundwater.
  The strata of certain regions contain radioactive elements, and heat emitted by this process may heat groundwater and produce hot springs.
In many parts of the world spring waters are believed to cure certain diseases. In Uganda, spring waters are believed to have a super-natural power to cure all sorts of ailments

## Slide 16: Open wells- Hand dug wells
These are the oldest and most widely used wells through out the world. They are excavated by hand or by a variety of unspecialized excavation equipment.
Digging is carried out until water comes out. Such wells are usually cylindrical with varying diameters, one to three meters being usual.
The depth to which a well should be dug largely depends on the type of groundwater table.
Private wells generally are less than 10 meters deep
The depth below the water table is normally up to 3 meters, due to the extreme difficulty of digging below the water table.

## Slide 17: Advantages of a hand dug well
Relatively unskilled and inexperienced persons can usually construct it.
No special tools or equipment's are required, except in difficult localities.
The well provides a reservoir for storage in addition to the water source.

## Slide 18: Disadvantages of a hand-dug well
The possibility of a hand-dug well caving, where casing is not adequate, is very high.
Another possible hazard is asphyxiation, a very real danger for the people who dig the well.
Such a well cannot be dug in a rocky locality without the use of special equipment or explosives.

## Slide 19: Bored well
This is a well constructed with special boring equipment operated by hand.
For a reliable yield, the minimum depth of a bored well should be around 6 meters but this depends very much on the level of the water table of an area.
The most common boring equipment is the auger or earth-auger. Augers are made with varying diameters, the so-called small-diameter auger being usually 8-10 cm in diameter.

## Slide 20: Advantage
The main advantage of this method is that the construction can be completed in a very short time and in geologically favorable areas.
Is suited for rapid mass construction

## Slide 21: Protection of groundwater from contamination
The techniques of protecting groundwater from contamination are based on a good understanding of the geology, topography, drainage basin, vegetation and human habitation of the locality
The rate of contamination of groundwater by pathogenic organisms or by dangerous chemical pollutants depends upon the following factors:
The nature of the aquifer: in particular the permeability of the ground formation in relation to contaminants flowing towards the water.

## Slide 22
The hydraulic gradient: this is the slope where water finds the easiest way to flow.
The depth to the water table: If the water table is high and near ground level, there will be less chance for the pathogenic organisms to be filtered out before the contaminated water reaches the water table
Distance from the source of contaminants: It is obvious that the further away the water source is from the sources of contaminants, the less is the chance for contamination. The most important source of contaminants for groundwater is human excreta, reaching the water source in the form of sewage, septic tank effluents, or leaching out from pit privies,etc.

## Slide 23: Ways in which well water/springs may be contaminated
Contaminants may infiltrate into the well from nearby, cess pools, septic tanks etc.
Polluted surface water (flood) may enter the well at or near the top or mouth of the well.
Pollutants such as dirt carrying viable micro-organisms, insects, and small animals may fall into the well if it has no cover.
Use of an unsanitary bucket and ropes may contaminate the well water.

## Slide 24: Prevention of contamination of a well
The well should be situated on a higher level than the source of contaminants– privies, cesspits, etc. In other words, the natural flow of the groundwater (the hydraulic gradient) should be from the well towards the source of contaminants; never vice versa.
In a normal soil formation, the minimum distance between the well and the source of contaminants should not be less than 15 meters.

## Slide 25: Protection of the well
Casing: the inside wall of the well should be made water proof by cementing from the top of the well down to a minimum depth of 3 meters. The deeper it is extended, the better. The casing of the well should also be extended for a minimum of 60cm above the surrounding ground level.
Cover: A concrete cover should be fitted over the casing to prevent dust, insects, small animals, etc. from falling in to the well and also to prevent leakage of flushed water.
Sanitary water drawing device: Ideally, a pump should be installed, but if a pump is not available a sanitary bucket and rope system should be used
Fencing: The immediate area of the well should preferably be fenced to keep animals away.
Diversion ditch: The area surrounding the well should be graded off in order to prevent the flow of storm water into the well.

## Slide 26: Surface Water
Surface water is found non-uniformly distributed over the earth’s surface.
As the rain reaches the surface of the earth, it becomes surface water or runoff. Surface water includes rivers, streams, lakes, ponds, etc.
The quantity and quality of surface water depend upon the conditions of the surface or catchment area over which it flows.

## Slide 27: Rain water
In regions where rainfall is abundant and frequent, rainwater can be a good source of water supply for individual families and for small communities.
The storage of rainwater is particularly important in areas with a long dry season. It can be stored in cisterns/tanks or ponds.
In some rural sections of Uganda, cistern water is used for all domestic and farm purpose, including drinking.
This is particularly true where groundwater is difficult to obtain.

## Slide 28: Advantages of Rainwater
It is a reliable source even if it rains once or twice a year only.
It is cheap and a safe means of water supply that may not need pipes or pumps and is available at the doorstep.
Its storage needs no fuel, no spare parts, but only very little skill to construct and maintain.
Women and children, who are normally water carriers in Uganda and other African countries, will be relieved of the burden of walking long distances to fetch inadequate supply.
Since rainwater is soft, little soap is needed for laundry purposes.

## Slide 29: Advantages of Rainwater
Since the cistern will be in a closed container, it will not permit spreading of diseases which are often found in an unprotected source such as rivers or ponds.
It is a system that can be used even in arid and semi-arid areas.

## Slide 30: Ocean Water
Ocean water is unfit for human consumption even though it comprises the largest portion of water on the earth's surface.
It is also too salty for irrigation and for domestic purposes.
To make the ocean water fit for these purposes; it must pass through a process known as desalination (a process of removal of salt from water). However, it is too expensive to consider.

## Slide 31: Major sources of water contamination in Uganda
Urbanization: Urbanization generally leads to higher phosphorus concentrations in urban catchments
Increasing imperviousness, increased runoff from urbanized surfaces, and increased municipal and industrial discharges all result in increased loadings of nutrients to urban streams.
Sewage and other Oxygen Demanding Wastes: Management of solid waste is not successful due to huge volumes of organic and non-biodegradable wastes generated daily.
As a consequence, garbage in most parts ofUganda is unscientifically disposed and ultimately leads to increase in the pollutant load of surface and groundwater courses.

## Slide 32: Major sources of water contamination in Uganda
Industrial Wastes: Many of the industries are situated along the banks of river such as steel and paper industries for their requirement of huge amounts of water in manufacturing processes and finally their wastes containing acids, alkalies, dyes and other chemicals are dumped and poured down into rivers as effluents.
Chemical industries concerning with manufacture of Aluminium release large amount of fluoride through their emissions to air and effluents to water bodies

## Slide 33: Major sources of water contamination in Uganda
Agro-chemical Wastes: Agro-chemical wastes include fertilizers, pesticides which may be herbicides and insecticides widely used in crop fields to enhance productivity.
Improper disposal of pesticides from field farms and agricultural activities contributes a lot of pollutants to water bodies and soils.
Thermal pollution: Changes in water temperature adversely affect water quality and aquatic biota. Majority of the thermal pollution in water is caused due to human activities

## Slide 34: Major sources of water contamination in Uganda
Climate Change: Global warming has also an impact on water resources through enhanced evaporation, geographical changes in precipitation intensity, duration and frequency (together affecting the average runoff), soil moisture, and the frequency and severity of droughts and floods.
Acid rain pollution: Water pollution that alters a plant’s surrounding pH level, such as due to acid rain, can harm or kill the plant.
Atmospheric Sulfur dioxide and nitrogen dioxide emitted from natural and human-made sources like volcanic activity and burning fossil fuels\interact with atmospheric chemicals, including hydrogen and oxygen, to form sulfuric and nitric acids in the air.
These acids fall down to earth through precipitation in the form of rain or snow. Once acid rain reaches the ground, it flows into waterways that carry its acidic compounds into water bodies.
Acid rain that collects in aquatic environments lowers water pH levels and affects the aquatic biota.

## Slide 35: General prevention approaches to water contamination
Improper use of fertilizers, herbicides and pesticides in farming should be stopped and organic methods of farming should be adopted
There should be ban on washing of clothes and laundry alongside the river banks and water sources.
Industries should install Effluent Treatment Plant (ETP) to control the pollution at source.
All towns and cities must have Sewage Treatment Plants (STPs) that clean up the sewage effluents.

## Slide 36: General prevention approaches to water contamination
Making people aware of the problem is the first step to prevent water pollution. Hence, importance of water and pollution prevention measures should be a part of awareness and education programme.
Polluter pays principle should be adopted so that the polluters will be the first people to suffer by way of paying the cost for the pollution. Ultimately, the polluter pays principle should be designed to prevent people from polluting and making them behave in an environmentally responsible manner.
Increase funding for municipal waste water management

## Slide 37: Water associated diseases
Water-associated disease can be defined as a disease in relation to water supply and sanitation. There are four categories:
  Waterborne disease
  Water-washed disease
  Water-based disease
  Water-related disease

## Slide 38: Waterborne diseases
Several infections enteric or intestinal diseases of man are transmitted through water contamination by fecal matter.
Pathogens excreted in water by an infected person include all major categories such as bacteria, viruses, protozoa and parasitic warms. Water acts only as a passive vehicle for the infectious agent.
To prevent the occurrence of waterborne diseases, water treatment is very essential.

## Slide 39: Examples of water born diseases
Types of organism | Disease Types
Bacteria | Typhoid and paratyphoid fever Cholera Diarrheas (caused by salmonella, yersinia entrocolitica, E.coli) Campylobacter dysentery Bacillary dysentery (caused by shigella
Virus | Hepatitis A Poliomyelitis Viral gastroenteritis
Protozoa | Amoebic dysentery Giardia (lambliasis) Balantidiasis
Helminthes | Helminthiasis caused by Ascaris and Trichinas

## Slide 40: Water-washed diseases
These comprise diseases linked to a lack of water for personal hygiene. Examples of water -washed diseases are:
Dermatological disease such as scabies
Ophthalmic disease such as trachoma and conjunctivitis
Louse-borne diseases such as louse borne typhus and relapsing fever.
Lack of good personal hygiene and unability to wash clothes encourages the proliferation of lice and the problems associated with their presence (itching, scratching, skin sores).
To prevent this type of disease, provision of an ample amount of water and personal hygiene are very essential.

## Slide 41: Water-based diseases
These are diseases caused by infectious agents that are spread by contact with water. The essential part of the life cycle of the infecting agent takes place from an aquatic animal.
A number of diseases depend upon the pathogenic organisms spending part of their life cycle in water or in an intermediate host which lives in water. Thus, infection of humans cannot occur by immediate ingestion of, or contact with, the organism excreted by sufferers
Many of the diseases in this class are caused by worms, which infest the sufferer and produce eggs, which are then discharged in feces or urine.
Typical examples are schistosomiasis and dracunculiasis (guinea worm).

## Slide 42: Water-based diseases
To prevent this group of diseases, the following methods may be implemented:
  Avoidance of contact with and ingestion of contaminated water.
  Reduction of intermediate hosts (snail)
  Storage of water from 24 to 72 hours to kill the cercaria.

## Slide 43: Water-related diseases
These are diseases transmitted by insects that live close to water Infections are spread by mosquitoes, flies and other insects that breed in water or near it.
There are a number of diseases which are spread by insects that breed or feed near water so that their incidence can be related to the proximity of suitable water sources.
Infection with these diseases is in no way connected with human consumption or contact with the water.

## Slide 44: Water-related diseases
Example: Malaria, sleeping sickness, yellow fever, onchocerciasis, etc.
To prevent this type of disease, making the water unsuitable for breeding of insects is essential.

## Slide 45
Thank you Very Much