## Slide 1: PRIMARY HEALTH CARE
wichealmicheal1@gmail.com

## Slide 2: Water and water supply
Duties of a clinical officer in water supply
Health educate communities about disease related to water supplies
Inspect water sources to detect possible sources of pollution/contamination
Facilitate communities to select and train water and sewage cooperation
Liaise with other authorities in matters related to water
Enforce the laws related to water sources
Initiate programs related to water sources
Participate in control of water related diseases (treatment)

## Slide 3: Underground water
Means of trapping underground water
Springs
Wells
Boreholes
Advantages of underground water
Free from pathogenic organisms
Used without farther treatment
Present in rural areas
Practical and economic easy to obtain.
Disadvantages
Have high mineral contents and therefore bound to be very hard.
Requires pumping.

## Slide 4
Types of springs
Shallow springs
Water which is held above the first impervious layer/ stratum and which emerges where the stratum out drops.
Characteristics of shallow springs.
May be constant or intermittent
Clayish in appearance
Contain suspended matter
Contaminated with surface or subsoil from pit latrines and refuse pits.
Characteristics of deep springs
Permanent
Water clear and sparkling
Water is filtered
Water is generally cool

## Slide 5: Spring protection
Purpose of protecting springs.
Protect the spring from pollution
Increase spring water yield.
Protect the environment
To improve assess.
Done by constructing a concrete wall to act as a barrier and outlet pipe for the water to be used, a storm water drain around the catchment area.

## Slide 6: Factors to consider before protecting a spring
Number of people
Quality and quantity of water
Access and distance
Location (the nature of the ground)
Pollution and contaminations around the source
Cost of the protection
Ownership of the land
Distance from the latrine (500m)
Source funds and resources

## Slide 7: Detailed spring protect
Community entry
Identify the spring
Survey the spring
Mobilization
Contact local leader
Sensitization
Select water source committee
Train them
Collect locally available materials, plan for action and labour
Clear up the site
Open up the waste water drain
Make a diversion trench for all running water

## Slide 8
Ix. Lay a foundation and platform of concrete using a ratio of 1:2:4 all to set for 1-3 days
X. Construct a retention wall, wing walls and steps (cement mortar ration 1:3)
xi. Insert delivery pipe at the level of the eyes (pipe 50mm diameter), galvanized iron pipe then insert a polyvinyl chloride pipe to prevent corrosion of the galvanized pipe.
xii. Insert a granite stone in the platform to prevent erosion of the concrete by the water
xiii. Plaster the floor but steps should remain rough to avoid falling off.
xv. Make the clay stone bended channels to lead water from eyes to pipe and there after cover with big stones.
Cover the stones with clay and thereafter soil.
NB. You can use polythene paper instead of clay then backfill with soil.

## Slide 9
xvii. Dig catchment drain/storm drain which joins the waste water (to limit soil erosion)
Plant grass on the catchment area and fence spring.
xx. Provision for washing may be made and animals to drink at a lower end point.
xxi. Sensitization of the community/committee of their roles and responsibilities then hand over of the water source to them.

## Slide 10: Summary for mobilization for spring protection and implementation
Identification
Spring survey
Contact local leader
Programme to meet the community
Meeting community
Select water source
Train water source committee
Plan and mobilize resources for use.
Implement the activity
Evaluate
Re-plan incase of any problem/failure
Make a report

## Slide 11: Spring
Can seasonal or permanent
Protection
Quality of water physical test then other conditions of spring virgin/dilapidated

## Slide 12: Factors consider when selecting WSC
Number of water committee number should be six , 3 women or more
The treasurer should be a woman
Should be a caretaker selected from this committee
Should be permanent residents of the area
Be users
Honest and good mobilizer

## Slide 13: Roles and responsibilities of water source committee.
Mobilize for funds/ labour and materials
Organizing meetings for purposes of sensitization
Keeping records
Reporting breakdowns
Facilitating setting of byelaws
Health education of matters concerning hygiene and sanitation
Maintain the water source clean
Ensuring hygiene practices around the water source
Selecting a caretaker
Mobilizing for improvement of sanitation in the community

## Slide 14: Roles of the community
Slashing and weeding around
Installing waste water storm, water channel
Replacement of worn-out pipes.
Repair of steps and retention walls
Provision of unskilled labour.
Treatment of water
Boiling
Filtering
Sedimentation
Storage
Chemical
Aeration
Freezing

## Slide 15: Well
Is a hole dug into the earth crust to depth below water bearing aquifer (saturation) for the purpose of obtaining ground.
Ways of constructing a well
Hand dug wells
Bored wells
Drilled wells
X-ctics of areas with water
Anthill
Palm trees
Adequate grass

## Slide 16: General sanitary requirements for wells
Situated as to prevent pollution
The ground adjourning well should be for a distance not less than 4(1.2m) all round covered with a water light paving construction so as to slope a way from the well.
The sides of the well should be rendered impervious for a depth that will prevent the contamination through the adjourning ground. If the well is lined with cement concrete or brick it should have a backing of puddle clay. This should make the lining more water tight.
The top of the well should be covered with concrete raised not less than 6 (150mm) from the paving and the cover should be tight fitting.

## Slide 17
The lower end of the pipe lid be at least 2( 600m) from the bottom of the well and provided with a strainer/ filter.
Water is to be drawn with bucket provided with;
  Efficient hinged cover
  A stand for the bucket not less than 6(150mm) above the level of paving contamination of shallow wells can occur from two source in addition to pollution of water .
  At the well head
  Stagnant water around the upper part of the well

## Slide 18: Protection of contaminations
Exclusion of surface drainage into water by pavement of 4(1.2m) all around the well.
All sources of contaminations should be away from the source (30m)
Arrangement to drain away water wastes must be made.
The wall of the well must be constructed of impervious materials
Method of pumping and raising water out of well must be installed.
Samples of physical , chemical and bacteriology analysis must be made regularly monthly.